## Slide 1: FERC Order 676j Managed Encumbrance
2023 G&I Training

## Slide 2: Managed Encumbrance

## Slide 3: FERC Order 676j – Managed Encumbrance and Dynamic Notifications
Managed Encumbrance
  An allocation of unconditional (not subject to Preemption) Firm Transmission Services that is set-aside in part or full and is treated in a manner similar to firm scheduled use of reserved capacity.
Dynamic Notifications
  The Notification Entry has been updated to show the e-mail addresses in list format, allowing OASIS users to easily add/delete rows

## Slide 4: Adding New Managed Encumbrance – Untagged Pseudo-Ties

## Slide 5: New Managed Encumbrance
  Log onto OASIS
  Click on the Transactions dropdown
  Select either Encumbrances or Encumbrance Request Summary

## Slide 6: New Encumbrance Request
  When clicking on the icon an Encumbrance Request Entry box will open
  Enter the Encumbrance Information by
    Selecting the Transmission Provider from the dropdown
    Selecting NEW in the Encumbrance Ref dropdown
  Once the Encumbrances or Encumbrance Request Summary is open
  Click on the icon

## Slide 7: New Encumbrance Request
  Once the Encumbrance Information has been chosen the Encumbrance Details and Encumbrance Profiles will pop up to be filled in

## Slide 8: New Untagged Pseudo Tie Using PTP
  Fill in required boxes
    Select Customer
    Reduction Type: UNTAGGED_PSEUDO_TIE
    Select Pseudo-Tie ID from the dropdown
    Fill in the POR/POD (Path will the auto populate), Start/Stop Time and MWs
    Enter the PTP TSR number in the Encumbered Ref box
    Click the Submit button

## Slide 9: New Untagged Pseudo Tie Using NITS TSR
  Fill in required boxes
    Select Customer
    Reduction Type: UNTAGGED_PSEUDO_TIE
    Select Pseudo-Tie ID from the dropdown
    Fill in the POR/POD (Path will the auto populate), Start/Stop Time and MWs
    Enter the NITS TSR number in the Encumbered Ref box
    Click the Submit button

## Slide 10: New Untagged Pseudo Tie Using NITS Application Number
  Fill in required boxes
    Select Customer
    Reduction Type: UNTAGGED_PSEUDO_TIE
    Select Pseudo-Tie ID from the dropdown
    Fill in the POR/POD (Path will the auto populate), Start/Stop Time and MWs
    Enter the NITS Application number in the Encumbered Ref box
    Enter the Encumbered Resource name exactly as registered
    Click the Submit button

## Slide 11: New Untagged Pseudo-Tie Using NITS Application Number
  Use of NITS Application Number and NITS Resource Errors
  Must enter the correct NITS Application number in the Encumbered Ref box
  Must enter the Encumbered Resource name as registered in webTrans Application Detail – NITS Resource Description
  If either are entered incorrectly a Data Entry Error will pop up

## Slide 12: New Untagged Pseudo-Tie Using NITS Application Number
  Use of NITS Application Number and NITS Resource Errors
  Must enter the Encumbered Resource name as registered in webTrans Application Detail – NITS Resource Description
  If entered incorrectly a Data Entry Error will pop up

## Slide 13: Modify Untagged Pseudo-Tie
  When clicking on the icon an Encumbrance Request Entry box will open
  Enter the Encumbrance Information by
    Selecting the Transmission Provider from the dropdown
    Selecting the Encumbrance Ref number from the dropdown
    Selecting the Action MODIFY
  Once the Encumbrances or Encumbrance Request Summary is open
  Click on the icon

## Slide 14: Modify Untagged Pseudo Tie
  Fill in required boxes
    Only editable information will be in the Encumbrance Profile area
      Start/Stop, MW, Encumbered Ref, and Encumbered Resource
    Click the Submit button

## Slide 15: Encumbrances
  All Approved Encumbrances will be populated in the Encumbrance page
  In the Composite Mode
    Encumbrance Ref Number
    Posting Ref Number
    Capacity Encumbered

## Slide 16: Encumbrances
  All Approved Encumbrances will be populated in the Encumbrance page
  In the Detailed Mode
    Encumbrance Ref Number
    Posting Ref Number
    Capacity Encumbered
    Encumbered Ref
    Encumbered Resource

## Slide 17: Encumbrances
  Filtering for more specific Encumbrance
  Clicking on the icon will open the Filtering Option
    Ability to change the view Mode to either Composite or Detailed

## Slide 18: Encumbrance Request Summary
  All NEW and MODIFIED Encumbrances will be populated in the Encumbrance Request Summary page
  The Posting Ref number associated for each Encumbrance Ref number
    Each time a modification is made to an Encumbrance Ref there will be a new Posting Ref number given to it
    The last Approved Posting Ref number will be the one associated with the Encumbrance Ref number on the Encumbrance page

## Slide 19: Encumbrance Request Summary Continued
    Highlighted Encumbrance Ref number have Provider Approval (Y)
    Un-Highlighted Encumbrance Rev number are NOT Approved (N) or in Review (R)
    Each Posting Ref and Encumbrance Ref posts the Pseudo Tie ID associated with it
    Each Posting Ref and Encumbrance Ref posts the Encumbered Ref associated with it

## Slide 20: Encumbrance Ref Actions
  Clicking on the Encumbrance Ref number from either the Encumbrance tab or the Encumbrance Request Summary tab
  Opens a new Encumbrance tab for just that specific Encumbrance Ref number
  Clicking on an Encumbrance Ref opens just that Posting Ref number

## Slide 21: Posting Ref Actions
  Detailed Posting Ref Data
  Clicking on the Posting Ref number will open a new tab with that specific Encumbrance Request detailed data
  Clicking on the Encumbered Ref number located in the Encumbrance Request Profile will open the Transmission Reservation Detail

## Slide 22: Encumbrances
  Transmission Reservation Detail
  Clicking on the MW Grant in the TSR Information
  Opens the Reservation Profile Detail of the Encumbered MWs

## Slide 23: Encumbrances
  Reservation Profile Detail
  Shows Available MWs
  Granted MW
    Show the Encumbered MWs along with the type of Encumbrance
      NOTE – The Encumbered MWs are not cumulative
    NET remaining MWs

## Slide 24: Dynamic Notifications
Dynamic Notifications
The Notification Entry has been updated to show the e-mail addresses in list format, allowing OASIS users to easily add/delete rows.
  Change Impacts – Notification (Admin > Notification).

## Slide 25: Questions
Contact:
    John Marhoefer
    JMarhoefer@misoenergy.org
    317-249-5306
    Darrin Landstrom
    DLandstrom@misoenergy.org
    651-632-8524